## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 12 – Memory Hierarchy/Direct-Mapped Caches
Instructors:
Mike Franklin
Dan Garcia
http://inst.eecs.berkeley.edu/~cs61c/fa11

## Slide 2: In the news…
Financial institutions may soon change what they trade or where they do their trading because of the speed of light
…first solution, published in 2010, considered the various latencies in global fiber-optic links and mapped out where the optimal points for financial transactions to originate - midway between two major financial hubs to maximize the chance of "buying low" in one place and "selling high" in another.
That means that out-of-the-way places - at high latitudes or mid-ocean island chains - could in time turn into global financial centers.
http://www.bbc.co.uk/news/science-environment-12827752
(from March 2011)
“Stock trades to exploit speed of light, says researcher”

## Slide 3: Agenda
Context – Remember the Great Ideas!
A Performance Teaser
Memory Hierarchy Overview
The Principle of Locality
Direct-Mapped Caches

## Slide 4: 6 Great Ideas in Computer Architecture
Layers of Representation/Interpretation
Moore’s Law
Principle of Locality/Memory Hierarchy
Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 5: 6 Great Ideas in Computer Architecture
Layers of Representation/Interpretation
Moore’s Law
Principle of Locality/Memory Hierarchy
Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 6: Defining Performance
What does it mean to say X is faster than Y?
2009 Ferrari 599 GTB
  2 passengers, 11.1 secs for quarter mile (call it 10sec)
2009 Type D school bus
  54 passengers, quarter mile time? (let’s guess 1 min)
http://www.youtube.com/watch?v=KwyCoQuhUNA
Response Time or Latency: time between start and completion of a task (time to move vehicle ¼ mile)
Throughput or Bandwidth: total amount of work in a given time (passenger-miles in 1 hour)

## Slide 7: Cloud Performance: Why Application Latency Matters
Key figure of merit: application responsiveness
  Longer the delay, the fewer the user clicks, the less the user happiness, and the lower the revenue per user

## Slide 8: Components of a Computer
Processor
Control
Datapath
Memory
Devices
Input
Output
Cache
Main Memory
Secondary Memory
(Disk)
Fast and Small
Slow and Large

## Slide 9: Storage in a Computer
Processor
  holds data in register file: 100’s of bytes
    (e.g., MIPS has 32 x 4 bytes)
  Registers accessed on sub-nanosecond timescale
Memory (a.k.a. “main memory”)
  More capacity than registers (~Gbytes)
  Access time ~50-100 ns
  Hundreds of clock cycles per memory access!

## Slide 10: Motivation:Processor-Memory Gap
“Moore’s Law”
DRAM
7%/year
(2X/10yrs)
Processor-Memory
Performance Gap (grows 50%/year)
µProc
55%/year
(2X/1.5yr)
1989 first Intel CPU with cache on chip
1998 Pentium III has two cache levels on chip

## Slide 11: Memory Hierarchy
If level closer to Processor, it is:
  Smaller
  Faster
  More expensive
  Retains a subset of the data from the lower levels (e.g., contains most recently used data)
Processor accesses data out of highest levels
Lowest Level (usually disk) contains all available data (does it go beyond the disk?)

## Slide 12: Typical Memory Hierarchy
Second
Level
Cache
(SRAM)
The Trick: present processor with as much memory as is available in the cheapest technology at the speed offered by the fastest technology
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
ITLB
DTLB
Speed (#cycles): ½’s 1’s 10’s 100’s 10,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Cost: highest lowest
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 13: Characteristics of the Memory Hierarchy
Increasing distance from the processor in access time
L1$
L2$
Main Memory
Secondary Memory
Processor
(Relative) size of the memory at each level
Inclusive– what is in L1$ is a subset of what is in L2$ is a subset of what is in MM that is a subset of is in SM
4-8 bytes (word)
1 to 4 blocks
1,024+ bytes (disk sector = page)
8-32 bytes (block)
Notes: Because the upper level is smaller and built using faster memory parts, its hit time will be much smaller than the time to access the next level in the hierarchy (which is the major component of the miss penalty).

## Slide 14: Cache (“$”) Concept
Mismatch between processor and memory speeds leads us to add a new level: a memory cache
Implemented with same IC processing technology as the CPU, integrated on-chip: faster but more expensive than DRAM memory
Cache is a copy of a subset of main memory
Modern processors have separate caches for instructions and data, as well as several levels of caches implemented in different sizes and technologies (e.g., processor vs. SRAM)

## Slide 15: Why Does the Hierarchy Work?
Principle of Locality: Programs access small portion of address space at any instant of time

## Slide 16: Library Analogy
Writing a report on a specific topic.
  E.g., works of J.D. Salinger
While at library, check out books and keep them on desk.
If need more, check them out and bring to desk.
  But don’t return earlier books since might need them
  Limited space on desk; Which books to keep?
You hope this collection of ~10 books on desk enough to write report, despite 10 being only 0.00001% of books in UC Berkeley libraries

## Slide 17: Two Types of Locality
Temporal Locality (locality in time)
  If a memory location is referenced then it will tend to be referenced again soon
   Keep most recently accessed data items closer to the processor
Spatial Locality (locality in space)
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
   Move blocks consisting of contiguous words closer to the processor
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.
+1 = 15 min. (X:55)

## Slide 18: Why Does the Hierarchy Work?
Principle of Locality: Programs access small portion of address space at any instant of time
What program structures lead to temporal and spatial locality in code?
In data?

## Slide 19: How is the Hierarchy Managed?
registers  memory
  By compiler (or assembly level programmer)
cache  main memory
  By the cache controller hardware
main memory  disks (secondary storage)
  By the operating system (virtual memory)
  Virtual to physical address mapping assisted by the hardware (TLB)
  By the programmer (files)

## Slide 20: Cache Design Questions
How best to organize the memory blocks of the cache?
To which block of the cache does a given main memory address map?
  Since the cache is a subset of memory, multiple memory addresses can map to the same cache location
How do we know which blocks of main memory currently have a copy in cache?
How do we find these copies quickly?

## Slide 21: Cache Basics: Direct Mapped
Direct mapped
  Each memory block is mapped to exactly one block in the cache
    Many lower level blocks share a given cache block
  Address mapping:
    (block address) modulo (# of blocks in the cache)
    Tag associated with each cache block containing the address information (the upper portion of the address) required to identify the block (to answer Q3)

## Slide 22: Caching Terminology
When reading memory, 3 things can happen:
  cache hit: cache block is valid and contains proper address, so read desired word
  cache miss: (Case 1 – cache block is empty/invalid) nothing in cache in appropriate block, so fetch from memory
  cache miss: (Case 2- block replacement) wrong data is in cache at appropriate block, so discard it and fetch desired data from memory (cache always copy)

## Slide 23: Caching: A Simple First Example
00
01
10
11
Cache
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Main Memory
Tag
Data
Q: Is the mem block in cache?
Compare the cache tag to the high order 2 memory address bits to tell if the memory block is in the cache
Valid
One word blocks
Two low order bits define the byte in the word (32b words)
Q: Where in the cache is the mem block?
Use next 2 low order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
(block address) modulo (# of blocks in the cache)
Index
Notes: For class handout

## Slide 24: Caching: A Simple First Example
00
01
10
11
Cache
Main Memory
Q: Where in the cache is the mem block?
Use next 2 low order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q: Is the mem block in cache?
Compare the cache tag to the high order 2 memory address bits to tell if the memory block is in the cache
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits define the byte in the word (32b words)
(block address) modulo (# of blocks in the cache)
Index
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 25: TIO: Mapping the Memory Address
Lowest bits of address (Offset) determine which byte within a block it refers to.
Full address format:
n-bit Offset means a block is how many bytes?
n-bit Index means cache has how many blocks?
Tag
Memory Address
Index
Offset

## Slide 26: TIO: Breakdown- Summary
All fields are read as unsigned integers.
Index
  specifies the cache index (which “row”/block of the cache we should look in)
  I bits <=> 2I blocks in cache
Offset
  once we’ve found correct block, specifies which byte within the block we want (which “column” in the cache)
  O bits <=> 2O bytes per block
Tag
  the remaining bits after offset and index are determined; these are used to distinguish between all the memory addresses that map to a given location

## Slide 27: Direct Mapped Cache Example
One word (4 Byte) blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
What kind of locality are we taking advantage of?
20
Data
32
Hit
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 28: Summary
Wanted: effect of a large, cheap, fast memory
Approach: Memory Hierarchy
  Successively lower levels contain “most used” data from next higher level
  Exploits temporal & spatial locality
  Do the common case fast, worry less about the exceptions (RISC design principle)
Direct Mapped Caches as the first “programmer-invisible” layer of the memory hierarchy